BioFridge Applications

Massive Transfusion Protocol – The BioFridge can be incorporated into your Massive Transfusion Protocol to move large quantities of blood quickly and safely while ensuring the blood will not be compromised.

Operating Room - In the surgery department during long and complicated cases where an immediate supply of blood may be required. The patient specific blood can be maintained in the room and readily available, if required.

Labor and Delivery - A readily available supply of blood can be maintained in Labor and Delivery for immediate access if required. The unit can easily be rolled into the room for easy access.

Patient Specific - Patient Specific Blood can be delivered to any department where it will be available if required. This eliminates the concern of providing the wrong blood to the patient. The blood is safely maintained in the BioFridge until it is required for patient use. If it’s not used it can be returned to the Blood bank with no concerns that it might have been compromised.

BioFridge System Justification

Reduces Blood Wastage - By maintaining the appropriate temperature ranges there will be no guess work regarding the viability of product returned to the Blood Bank. No matter where your blood is in the Hospital it will constantly be maintained within the appropriate temperature range for up to 18 hours on a full charge.

Notification of Temperature Excursions – With our optional Wi-Fi Temperature Monitoring System, you will have Real-time documentation verifying appropriate temperatures have been maintained. If the temperature does go out of range, you will be given notification so that you can intervene proactively and prevent product loss.  All data and corrective actions are recorded to meet your regulatory requirements and can be managed with our iPhone, iPad and Android Applications.

Simplifies Blood Cold Chain Transportation – Product is protected with appropriate temperature control as it moves around the hospital.

Massive Transfusion Protocol Improved - The BioFridge is the ideal product for moving large quantities of blood and Plasma quickly and efficiently. Numerous facilities have incorporated the BioFridge into their MTP.

Cools Warm Plasma – The unique design of the Thermal Mass Carrier (TMC) quickly cools warm plasma from 37c to 4c within 40 minutes using separate internal compartments. The TMC ensures that the cold Plasma does not affect the integrity of your already cold Red Blood Cells which can be transported in the same BioFridge unit.

Improves Quality Management – The BioFridge is Compliant with AABB and other accrediting agencies and can be a significant part of a comprehensive blood management program.